Comments:

- The folder “Material_parameters” is a working directory to extract material parameters. The value of the material parameters obtained should be included in the corresponding Excel file in the “3THBTSC” directory so that Jupyter-Notebook can easily find them.
- Data for the absorption coefficients are not always available for all the spectral range. We want to have data tabulated at least up to 4 eV. To this end, the last value known is assigned to photon energies of 4 eV when the latest is not available. We have also set the photon energy at which we consider the absorption coefficient to be zero. Take into account that the absorption coefficient we have to model here is the one that creates electron-hole pairs and not the one related to parasitic absorption such us free carrier absorption
- For the digitalization of the plots, when necessary, we have used Engauge digitizer (http://markummitchell.github.io/engauge-digitizer/)
Digitized files are also included in the directory (extension “dig”)

[1] GaAs absorption coefficient – High purity. (up to 1.6 eV)
[2]⁠⁠AlxGa1-xAs absorption coefficient for x=0.315, x=0.590 (pure material) Other values of x could be worked out in the future from this reference.
[3] ⁠Silicon absorption coefficient (pure) Taken form fig. 3 in the reference. (It is needed to improve the values for energies higher than 2.63 eV)
[4] CH3NH3PbI3 “perovskite” absorption coefficient.⁠

[1]	H. C. Casey, D. D. Sell, and K. W. Wecht, “Concentration dependence of the absorption coefficient for n- and p-type GaAs between 1.3 and 1.6 eV,” J. Appl. Phys., vol. 46, no. 1, pp. 250–257, Jan. 1975.
[2]	D. E. Aspnes, S. M. Kelso, R. A. Logan, and R. Bhat, “Optical properties of AlxGa1-x As,” J. Appl. Phys., vol. 60, no. 2, pp. 754–767, Jul. 1986.
[3]	H. A. Weakliem and D. Redfield, “Temperature dependence of the optical properties of silicon,” J. Appl. Phys., vol. 50, no. 3, pp. 1491–1493, 1979.
[4]	S. De Wolf et al., “Organometallic halide perovskites: Sharp optical absorption edge and its relation to photovoltaic performance,” J. Phys. Chem. Lett., vol. 5, no. 6, pp. 1035–1039, 2014.